## Slide 1: Team Details
Case Study No. 3 – Adaptive QoS Engine (PulseQoS)
Manas Girdhar (Team Leader)
Meenakshi Satpathy
Birla Institute of Technology, Mesra

## Slide 2: PulseQoS: the call never notices the download Intent-aware, self-verifying QoS controller for home broadband — payload-blind, built on open Linux tc
ARCHITECTURE — one closed loop, two speeds
UI
ANALYTICS
& CONTROL
DATA
EDGE
(router)
DEVICE &
NETWORK
Focus Mode app / REST API
manual intent or Zero-click auto-protect • 1-tap undo
Dashboard + “Why” panel
p95, jitter, loss, queue, Jain, RPM • Twin prediction vs real
FAST LOOP ≤ 1 s
capacity estimator
one-way delay
rate cuts act at
once, skip trial
SLOW LOOP 10–30 s
policy controller
safe action menu
hysteresis +
hold time
AI Experience Twin
predicts next-10 s
call delay for each
action; drops unsafe
ones before users feel
Safety gate
validate → live
trial → keep or
roll back • watchdog
→ safe state
Flow table (conntrack) • telemetry • versioned policy bundles • audit log • Twin training set
AI Conformal classifier
metadata only • boosts only
when certain, else Unknown
One mark per flow
class → conntrack mark
restored both ways (ctinfo)
Linux tc enforcement
CAKE on WAN + IFB
HTB variant for floors
Home devices (emulated)
laptop calls • console • 3 TVs • 15 GB download
WAN bottleneck (emulated)
token bucket + netem • 100 → 20 Mbps • IPv4/IPv6
DESIGN RULES THAT KEEP IT CORRECT
▸ Tins: call audio + gaming → Voice; call video → Video (Voice tin is only 25%; RFC 8837); Unknown never boosted
▸ Trust: Internet DSCP is cleared on arrival; only our own conntrack mark sets priority
▸ Link realism: overhead compensation, upload ACK filter, per-direction one-way delay
▸ Privacy & abuse: no payload or domain logging; LAN-only authenticated intent API with budgets
THE AI ONLY PULSEQOS HAS — each must beat a rule-based twin
1 Conformal classifier. Boosts a flow only when its prediction set is a single call/game class, so wrong boosts stay ≤ a chosen rate (e.g. 1%) by construction on calibration-like traffic. vs port rules
2 Experience Twin. Learned model of the home link (trained offline in the lab, never by exploring on users) predicts each change’s effect and rejects harmful ones before they go live. metric: harm-seconds avoided
3 Zero-click Focus. Detects a call starting on a busy link and protects it within seconds, charged to a Fairness Budget, with undo. metric: time-to-protection
No chatbot: the case asks AI to improve a measurable outcome, not add a chat interface. An AI part that loses its A/B test is switched off.
PILOT EVIDENCE — measured 27 Oct, not assumed
Chart: p95 call-probe delay during a 4-stream download (ms)
| FIFO (no QoS) | Class shaping (HTB)
p95 call-probe delay (ms) | 138 | 0.07
Download goodput identical: 18.7 of 20 Mbps — call protected, bulk not starved.
5 paired runs, Linux namespaces, 20 Mbit link; emulation without WAN delay, ideal classification. Round 2: CAKE, netem, 8 systems × 14 scenarios × 10 runs, incl. CAKE’s own autorate.
Boundary: reference implementation in emulation, labelled as such. A product also needs router hardware, flow-offload handling, gigabit CPU budget, Wi-Fi airtime fairness and certification.
Notes: 60-second pitch: Home links carry calls, games, TVs and downloads at once; big queues, not low bandwidth, ruin calls. PulseQoS runs on proven Linux CAKE with a fast loop that follows the real link speed within a second, and a slow, safety-gated loop for policy. Our AI layer is what nobody else has, and each part must beat a rule-based twin: a conformal classifier that only boosts traffic when it is certain, so wrong boosts stay under a chosen rate; an Experience Twin, a learned model of the home link that predicts the effect of every change and rejects harmful ones before users feel them; and Zero-click Focus, which protects a call the moment it starts, with a fairness budget and undo. Our pilot already shows the problem and the fix: a download pushed call delay to 138 ms on FIFO; class shaping kept it under 0.1 ms with the same download speed. In Round 2 we measure against CAKE and its autorate, not just against no QoS.