## Slide 1: Team Details
Case Study No. 3
Team MM
Manas Girdhar (Team Leader)
Meenakshi Satpathy
Birla Institute of Technology, Mesra

## Slide 2: PulseQoS: Adaptive Home QoS The call never notices the download. An adaptive QoS controller built on Linux tc and CAKE, with no payload inspection.
Key design decisions
Tins: call audio and games in Voice, call video in Video (Voice is capped at 25% in diffserv4).
Trust: DSCP from the Internet is cleared, so outside traffic cannot claim priority.
Two loops: a speed drop is handled within a second; policy changes pass a safety check first.
Privacy: no payload or domain logging; the intent API is LAN-only and needs a token.
UI
ANALYTICS
& CONTROL
DATA
EDGE
DEVICE &
NETWORK
Focus Mode app / REST API
protect a call for N minutes; auto-protect has undo
Dashboard
latency, jitter, loss, queue depth, fairness, reason per change
Rate loop (1 s)
estimates capacity from one-way delay; lowers shaper rate at once
Policy loop (10-30 s)
rule-based, fixed set of actions, hysteresis and hold time
Link model (ML)
predicts call delay per action; filters out risky ones
Safety check
short live trial, keep or roll back; watchdog falls back to CAKE
Flow table (conntrack), telemetry, versioned policies, audit log
Flow classifier (ML)
packet sizes and timing only; unsure flows stay best effort
Flow marking
class kept in conntrack mark, restored with ctinfo
Linux tc
CAKE on WAN and IFB; HTB variant for hard floors
Home devices (emulated)
laptop on a call, console, 3 TVs, a large download
WAN link (emulated)
netem + token bucket, 100 to 20 Mbps, IPv4 and IPv6
Where we use ML, and how we check it helps
1. Flow classifier: LightGBM with conformal prediction. A flow is prioritised only when the model is confident, keeping wrong boosts under a target rate (say 1%). Compared with port rules.
2. Link model: trained offline on lab runs; predicts how a policy change affects call delay, so risky changes are dropped before the live trial. Measured by bad-delay seconds avoided.
3. Auto-protect: a call starting on a busy link is protected automatically, within a daily per-device limit, with undo. Measured by time to protection.
Each ML part is tested against the rule-based version. If it does not improve the numbers, we drop it.
Early test we ran (27 Oct)
Chart: 95th percentile ping delay during a download (ms)
| No QoS (FIFO) | Class shaping (HTB)
95th percentile ping delay (ms) | 138 | 0.07
Same download speed in both (18.7 of 20 Mbps): the call was protected without starving the download.
2 Linux namespaces, 20 Mbit link, 4 TCP streams, 50 pings/s, 5 runs each, no WAN delay. Round 2 compares against CAKE, CAKE autorate and cake-autorate in 14 scenarios.
Notes: Talking points (about 1 minute): In a home, calls, games, TVs and downloads share one link. The real problem is queueing delay, not bandwidth. We build on CAKE in Linux rather than replacing it. On top of it we add a rate loop that follows the link speed every second, a rule-based policy loop that goes through a safety check and can roll back, and a way for the user to protect a call for a set time. ML is used in three places: the flow classifier, a link model that screens policy changes, and auto-protect for calls. Each one is compared with the rule-based version and dropped if it does not help. Our early test: during a download, ping delay was 138 ms with no QoS and under 0.1 ms with class shaping, with the same download speed. In Round 2 we compare against CAKE and its autorate tools, not only against no QoS.